## Slide 1: I/O Thin Clients Power Management

## Slide 2: Review
Memory-Mapped I/O
  Map all the control registers into the memory space
  Each control register is assigned a particular and unique memory address
DMA
  A memory address register
  A byte count register
  One or more control registers
  3 modes: Word-at-a-time, Block, Fly-by
Precise vs. Imprecise Interrupt
  Precise: Leave the machine in a well-defined state
    PC is saved in a known place
    All instructions before the one pointed to by the PC have fully executed
    No instruction beyond the one pointed to by the PC has been executed
    Execution state of the instruction pointed to by the PC is known
  Imprecise: Does not meet all requirements as precise

## Slide 3: Review
I/O Software
  Goals
    Device Independent, Error handling, Synchronous vs. Asynchronous, Buffering, Dedicated device allocation
  I/O with DMA
  Layers
    User level I/O software: pooling with daemon scheduling (Asynchronous)
    Device independent
      Uniform naming, Uniform interface, Independent block size
      Buffering
      Error handling, Dedicated device allocation
    Device Drivers: help OS control specified devices depending on standard interface
    Interrupt Handlers: handle interrupt to determine what the system should do

## Slide 4: Review
Disk arm scheduling
  Seek time
    FCFS: Process request sequentially
    SSF: the least movement of the disk arm from its current head position
    Elevator
      Approach: Arm moves in one direction only, satisfying all outstanding requests until it reaches the last track in that direction
      Implementation: When the highest numbered cylinder with a pending request has been services, the arm goes to lowest number cylinder with a pending request and then continues moving in an upward direction
  Rotational delay
    If two or more requests for the same cylinder are pending, the driver can issue a request for the sector that will pass under the head next
    The OS should maintain a pending request table for each drive, a seek should be issued to move its arm to the cylinder where it will be needed next
  Actual data transfer time (SATA)

## Slide 5: Review
Disk arm scheduling
  Error handling
    Bad sector
      Sectors do not correctly read back the value just written to them
      Controllers remap the bad sector to the spare and/or Shift all the sectors up one
      OS must first acquire a list of bad sectors, then it can build remapping tables
    Seek errors
      Move the arm as far out as it will go and reset the controller’s internal idea of the current cylinder to 0

## Slide 6: Review
Disk arm scheduling
  Disk Consistency
    Stable write: Write block on drive 1, then reading it back to verify. The driver 2 is written and reread until it succeeds
    Stable read: First read block on drive 1 in n times. If all of these give bad ECCs, reading on drive 2
    Crash recovery: scans both disks comparing corresponding blocks. Bad block is overwritten with the good blocks or block from driver 1 is written onto drive 2
    Optimizing: using Nonvolatile/ Volatile RAM to replace in using driver 2

## Slide 7: Review
Clocks
  02 types
    Using volt power
    a crystal oscillator, a counter, and a holding register
  2 modes: one shot mode, square wave mode
  Functions
    Maintaining the time of day (real time).
    Preventing processes monopolizing CPU
    Accounting for CPU usage
    Handling alarm system call
    Providing watchdog timers
    Doing profiling, monitoring, statistics gathering
User Interfaces
  Input software (Keyboard software: scan code, echoing, tab handling, device equivalent
  Output software (Text window, X Window, GUI, Bitmaps, Fonts)
  Mouse software

## Slide 8: Objectives
Thin Clients
Power Management

## Slide 9: Thin Clients
Is called THINC
The most users want high performance interactive computing, do not really want to administer a computer
The user machines had no software at all
Strip the client machine of all it smarts and software and just use it as a display, with all the computing done on the server side
The protocol between client and the server just tells the display how to update the video RAM, nothing more
On the server side, graphical programs use high level command to paint the screen. These are intercepted by THINC software and translated into commands that can be sent to the client. The commands may be reordered to improve efficiency

## Slide 10: Power Management Overview
There are 2 general approaches to reducing energy consumption
  The OS turn off parts of the computer when they are not in use because a device that is off uses little or no energy
  The application program to use less energy, possibly degrading the quality of the user experience, in order to stretch out battery time

## Slide 11: Power Management Hardware Issues
Batteries come in two general types
  Disposable: like AAA, D cells, can be used to run handheld, but do not have enough energy to power notebook computers with large bright screens
  Rechargeable
    Can store enough energy to power notebook for a few hours
    Includes Nickel and Lithium ion
The OS manages the state transition at the right moments to reduces energy consumptions
  On: the device can be used
  Off: not consumptions
  Sleeping: when the device will not be needed for a short time, the energy consumption is reduced
  Hibernate: when the device is not expected to be needed for a longer interval, the energy consumption is reduced more, but this state will takes more time and energy than getting it out of sleep state
Power manage bring ups a number of questions that the OS deal with
  Which devices can be controlled?
  Are they on/off, or do they have intermediate states?
  How much power is saved in the low-power states?
  Is energy expended to restart the device?
  Must some content be saved when going to a low-power state?
  How long does it take to go back to full power?

## Slide 12: Power Management OS Issues
The OS controls all devices and must decide what to shut down and when to shut down
  If it shuts down a device and that device is needed again quickly, there may be an annoying delay while it is restarted
  If it waits too long to shut down a device, energy is wasted for nothing
The trick is to find algorithms and heuristics that let the OS make “good” decision about what to shut down and when

## Slide 13: Power Management Display
The biggest spenders item of the energy budget
Many OS attempt to save energy here by shutting down the display when there has been no activity for some number of minutes
The user can often decide what the shutdown interval is, thus pushing the trade-off between frequent blanking of the screen and using the battery up quickly back to the user
Turn off the display is a sleep state because it can be regenerated (from the video RAM) almost instantaneously when any key is struck or the pointing device is moved
Improvement
  The display consist of some number of zones that can be independently powered up or down
  The window manage has to understand power management or be capable of accepting instructions from some other piece of the system that does

## Slide 14: Power Management Display
Tanenbaum, Fig. 5-46.
The inactive zone (zone out of pointer) can be dark
The active zone must be fitted into the minimize zone by the window managers using the snap-to-zone in automatically
→ reducing of power
More sophisticated, the window manager partial illuminate a window that was not completely full

## Slide 15: Power Management Hard Disk
Takes substantial energy to keep it spinning at high speed, even if there are no accesses
Many computer spin the disk down after a certain number of seconds or minutes of inactivity. When it is next needed, it is spun up again
A stop disk is hibernating because it takes quite a few seconds to spin it up again, which causes noticeable delays for the user
Restarting the disk consumes considerable extra energy
In practice, most systems are conservation and only stop the disk after a few minutes of inactivity
Disk cache in RAM is used
  If a needed block is in the cache, an idle disk does not have to be restart to read
  If a write to the disk can be buffered in the cache, a stopped disk does not have to restarted just to handle the write
  The disk can remain off until the cache fills up or a read miss happens
OS keeps running programs informed about the disk state by sending it messages or signals

## Slide 16: Power Management CPU
A notebook CPU can be put to sleep software, reducing power usage to almost zero.
  The only thing it can do in this state is wake up when an interrupt occurs
  Whenever the CPU goes idle, either waiting for IO for no work to do, it goes to sleep
The CPU voltage can often be reduced in software, which save energy but also reduces the clock cycle (approximately linearly). Since power consumed is proportional to the square of the voltage, cutting the voltage in half makes the CPU about half as fast but at ¼ the power
Running slowly is more energy efficient than running quickly

## Slide 17: Power Management Memory
There are 2 possible options
  The cache can be flushed and then switched off
    It can always be reloaded from main memory with no loss of information
    The reload can be done dynamically and quickly, so turning off the cache is entering a sleep state
  Write the contents of main memory to the disk, then switch off the main memory itself
    It is hibernation since virtual all power can be cut to memory at the expense of a substantial reload time, especially if the disk is off too
    When the memory cut off, the CPU either has to be shut off as well or has to cause it to jump to code in a ROM so the memory can be reloaded before being used
    Despite all the overhead, switching off the memory for long periods of time may be worth it if restarting in a few seconds is considered much more desirable than rebooting the OS from disk, which often takes a minute or more

## Slide 18: Power Management Wireless Communication
The radio transmitter and receiver required are often first-class power hogs
Solutions
  The mobile computers communicate with fixed base stations that have large memories and disks and no power constraint.
  Thus, this computer send a message to the base station when it is about to turn of the radio, then the base station buffers incoming messages on its disks
  When the mobile computer switches on the radio again, it tells the base station, then any accumulated messages can be sent to it
  Outgoing messages that are generated while the radio is off are buffered on the mobile computer. If the buffer threatens to fill up, the radio is turned on and the queue transmitted to the base station
When should the radio be switched off?
  Let the user or the application program decide
  Turn it off after some number of seconds of idle time
When should the radio be switched on?
  Let the user or the application program decide
  Switched on periodically to check for inbound traffic and transmit any queued message, or the output buffer is close to full

## Slide 19: Power Management Thermal Management
Modern CPUs get extremely hot due to their high speed
Desktop machines normally have an internal electric fan to blow the hot air out of chassis
With notebooks, the OS has to monitor the temperature continuously
  When it gets close to the maximum allowable temperature, the OS has a choice
  It can switch on the fan, which makes noise and consumes power
  It can reduce power consumption be
    Reducing the backlighting of the screen
    Slowing down the CPU
    Being more aggressive about spinning down the disk

## Slide 20: Power Management Battery Management
Smart batteries can also be instructed to change various operational parameters under control of the OS
Some notebooks have multiple batteries
  When the OS detects that one battery is about to go, it has to arrange for a graceful cutover to the next one, without causing any glitches during the transition
  When the final battery is on its last legs, OS warn the user and the cause an orderly shutdown making sure that file system is not corrupted

## Slide 21: Power Management Driver Interface
The Windows system has an elaborate mechanism for doing power management called Advanced Configuration and Power Interface – ACPI
The OS can send any conformant driver commands asking it to report on the capabilities of its devices and their current states
This feature is especially important when combined with plug and play because just after it is booted, the OS does not even know what devices are present, let alone their properties with respect to energy consumption or power manageability
It can also send commands to driver instructing them to cut their power levels

## Slide 22: Power Management Application Program Issues
Tell the programs to use less energy, even if this means providing a poorer user experience
This information is passed on when the battery charge is below some threshold. Then the program decide between degrading performance to lengthen batteries life or to maintain performance and risk running out of energy

## Slide 23: Summary
Thin Clients
Power Management
Q&A

## Slide 24: Next Lecture
Deadlock
  Problems & Solutions
Other Issues
  Live Lock
  Two phase Locking
  Communication Lock
  Starvation